## Slide 1
GENESIS
IDEATHON
Team Name – PHOENIX
Team Members – S Sahana[Leader][CB.EN.U4CHE25056],R Subashini[CB.EN.U4CHE25036],R Varunya[CB.EN.U4CHE25049],Naman Goyal[CB.EN.U4CHE25029]
Selected Domain – Domain 3
Problem Statement –The critical challenge is to develop a scalable and economically viable PFAS destruction pathway capable of overcoming the thermodynamic and kinetic stability of the C–F bond, enabling controlled defluorination and near-complete mineralization of PFAS , while minimizing energy demand, secondary contamination and hazardous transformation products.maining economically viable for large-scale deployment.
TEAM & DOMAIN

## Slide 2: DOMAIN PROBLEM
TEAM
Phoenix
WHY NOW? | WHAT NEEDS TO BE SOLVED?
Forever chemicals — Exceptional C–F bond stability enables long-term persistence and circulation in water systems | Break the backbone — Develop a pathway capable of overcoming PFAS’s highly stable C–F bonds.
Removal ≠ destruction — Adsorption and membranes often transfer PFAS into secondary waste rather than eliminate it. | Achieve true destruction — Progress beyond fragmentation to defluorination and mineralization.
Transformation risk — Incomplete degradation can generate persistent short-chain PFAS and other transformation products. | Prevent secondary hazards — Minimize persistent by-products and concentrated waste streams.
Scale-up gap — Existing destructive approaches can demand high energy, extreme conditions and specialized equipment. | Make it practical — Reduce energy, reagent cost and process complexity while maintaining high destruction efficiency.
India needs scalable remediation — Growing contamination demands solutions suited to large and diverse water streams. | Enable deployment — Achieve continuous operation, diverse-water compatibility and economic scalability.

## Slide 3: WHO IS AFFECTED?
TEAM
Phoenix
PFAS CONTAMINATION: TARGET GROUPS & BENEFICIARIES
1. Primary / Target Groups
  Communities exposed to PFAS-contaminated drinking water, soil, and food.
  Farmers and agricultural workers on potentially contaminated land.
  Vulnerable populations, including children and pregnant women.
2. Secondary Stakeholders
  Water treatment facilities and environmental testing laboratories.
  Government regulators and public health authorities.
  PFAS-using industries, agricultural producers, and researchers.
3. Key Beneficiaries
  Human health: Communities benefit from reduced PFAS exposure.
  Agriculture: Farmers, livestock, and consumers benefit from safer crops and food chains.
  Environment: Soil, groundwater, and aquatic ecosystems benefit from reduced contamination.
  Future generations: Benefit from preventing long-term PFAS accumulation.
4. Wider Impact
  Improved detection, monitoring, and treatment of PFAS contamination.
  Better management of contaminated agricultural land and crop residues.
  Stronger environmental protection and more sustainable industrial practices.

## Slide 4: CURRENT SITUATION & CONTEXT
TEAM
Phoenix
EXISTING SCENARIO: PFAS TREATMENT TODAY
From contaminant removal to complete destruction
BACKGROUND
Per- and polyfluoroalkyl substances (PFAS), known as forever chemicals, persist in water and the environment because their carbon–fluorine (C–F) bonds are exceptionally strong. Conventional water-treatment processes are generally ineffective at removing many PFAS.
HOW DOES TREATMENT WORK TODAY?
- Activated Carbon (GAC): Adsorbs PFAS onto porous carbon surfaces.
- Ion-Exchange Resins: Capture PFAS using specialized charged resins.
- Reverse Osmosis (RO): Separates PFAS from water using high-pressure membranes.
Emerging Destruction Technologies: Electrochemical oxidation, supercritical water oxidation and plasma-based processes aim to break down PFAS molecules.
THE CRITICAL GAP
Conventional technologies primarily separate PFAS from water rather than destroy it, producing contaminated filters, spent adsorbents or concentrated waste streams that require further management. Destruction technologies are promising but still face challenges involving energy demand, cost, scalability and by-product control.

## Slide 5: KEY CHALLENGES
TEAM
Phoenix
1) Exceptional C-F Bond Stability: The strong carbon-fluorine bonds make PFAS highly resistant to conventional chemical, biological and thermal degradation. 2) Removal Without Destruction: Activated carbon and ion-exchange resins capture PFAS but transfer contamination to spent media or concentrated brine. 3) High Energy and Treatment Costs: Advanced destruction technologies may require
substantial energy, specialized catalysts or complex operating conditions. 4) Incomplete Defluorination & Toxic By-products: Partial degradation can produce persistent short-chain PFAS or other potentially harmful intermediates instead of complete mineralization. 5) Practical Deployment Constraints: Treating low PFAS concentrations in real wastewater, while managing competing contaminants and minimizing secondary waste, remains challenging.

## Slide 6: EXISTING SOLUTIONS / APPROACHES
TEAM
Phoenix
1. Activated Carbon Adsorption Captures PFAS from water, but transfers contamination to spent carbon. Gap: Safe disposal or regeneration and actual PFAS destruction.
2. Ion-Exchange Resins Efficiently capture ionic PFAS, but regeneration produces concentrated waste brine. Gap: Effective treatment of residual PFAS without secondary waste.
3. Advanced Oxidation Processes (AOPs) Use reactive species to degrade contaminants, but conventional hydroxyl-radical-based methods struggle to break strong C–F bonds. Gap: Efficient, progressive defluorination.
4. Electrochemical & Plasma Treatment Can destroy PFAS, but may require high energy input and specialized equipment. Gap: Affordable, energy-efficient scale-up.
5. Advanced Reduction Processes Use powerful reducing species, such as hydrated electrons, to initiate C–F cleavage, but their generation and delivery can be challenging in real water matrices. Gap: Low-cost, selective and sustained electron transfer with minimal harmful intermediates.

## Slide 7: PROBLEM INSIGHTS & OPPORTUNITY AREAS
TEAM
Phoenix
Resources required to solve the problem
1. Hardware Requirements
- Laboratory glassware and sample containers
- Magnetic stirrer, pH meter and digital weighing balance
- Temperature-controlled reactor and UV light source
- Filtration unit or centrifuge
- LC-MS/MS facility for PFAS testing
- Safety equipment
2. Software Requirements
- Microsoft Excel – data recording and analysis
- Python – graphs and data analysis (optional)
- AutoCAD/SolidWorks – prototype design
- Arduino IDE – sensor monitoring (optional)
- PowerPoint/Canva – presentation
- Google Scholar/Scopus – research papers
3. Other Resources
Cerium oxide (CeO₂), water samples and
PFAS analytical standards
- Electrode materials (if required)
- University laboratory and PFAS testing facilities
- Chemicals, safety equipment and waste containers
- Research papers, technical references and project funding
4. Human Resources
- Chemical engineering and materials science students
- Environmental science expert
- Electronics student (optional)
- Laboratory technician and analytical chemistry expert
- Faculty mentor and team coordinator

## Slide 8: INITIAL DIRECTION & EXPECTED OUTCOME
TEAM
Phoenix
1. OUR PROPOSED INTERVENTION
Develop a CeO₂-enabled electrochemical treatment approach to investigate the degradation of persistent PFAS by targeting their exceptionally stable carbon–fluorine (C–F) bonds.
2. KEY AREAS OF IMPROVEMENT
- Destructive Efficacy: Advance beyond contaminant separation towards molecular degradation and defluorination.
- Energy Optimization: Investigate lower-potential operating conditions to improve energy efficiency.
- Environmental Integrity: Minimize secondary waste and mitigate harmful degradation by-products.
Deployment Feasibility: Explore cost-effective, modular implementation for Indian water-treatment infrastructure
OUR VISION
To transform PFAS remediation from contaminant containment into measurable, energy-conscious and sustainable destruction.
3. ANTICIPATED SUCCESS INDICATORS
- Quantifiable PFAS degradation and fluoride release.
- Improved energy efficiency per unit of PFAS destroyed.
- Reduced secondary-waste generation and controlled by-product formation.
- A technically validated pathway towards scalable implementation.
SUPPORTING DIGITAL INNOVATION: A PFAS Smart Treatment Optimizer App for comparative treatment analysis and preliminary cost–energy assessment.